## Slide 1: Pi Gate
Pied Piper Program
7th March 2018
DucThang, Nguyen
@thangndu

## Slide 2: Pi Gate System
Automated Gate System (Pi Gate)
  Automatic detect plate number
  Automatic display plate number
  Automatic/manual gate control
  Automatic alarm system (Light and Sound)
  Access gate system dashboard anywhere
  Github repository
  https://github.com/thangndu/pigate
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 3: Bill of Materials
ITEM | QUANTITY
Raspberry PI 3 Model B | 1
Raspberry PI Camera V2 | 1
Distance Sensor | 1
Step Motor (Micro Servo SG90) | 1
LCD 1602 + I2C Interface Module | 1
Speaker | 1
LED Module | 1
Buzzer Module | 1
Button Module | 1
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 4: System Architecture
Distance Sensor
(Car detection)
Step Motor
(Gate controller)
Camera
(Plate capture)
LCD
(Display)
Button
(Person control)
LED and Buzzer
(Alarm)
AWS Rekognition
(Laptop)
Boto3
(Plate recognition)
MQTT Broker
(PWS)
Redis
Flask
(Gate dashboard)
AWS S3
AWS Polly
Speaker
(Audio streaming)
(Raspberry Pi)
Location
API
Bootstrap
AWS Lambda
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 5: Pi Gate
Camera
Distance
Sensor
Gate
Display
Speaker
Led & Buzzer
Button

## Slide 6: Command Center
Detect car
Capture
plate number
Detect
plate number
Display
plate number
Gate
Speaker
Led & Buzzer
Button
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform

## Slide 7: Dashboard (piper.cfapps.io)

## Slide 8: Demo
Registered
plate number
Un-registered
plate number
Notes: Mention the Digital and IT Transformation: Modernize, AUTOMATE, Transform